## Slide 1: VIKASIT NAGPUR HACKATHON 2026
Project Name (Registered on portal): OrangeX
Registration No (Received on Whatsapp): PAR-260814-3389
Theme (Existing): Open Innovation for Vikasit Nagpur
Problem Statement Title (Existing): Local-resolution access to fragmented water-quality information
Expected Solution Title (Existing): Citizen-centric water transparency map
Designed Solution Title (Team): NeerNetra
Connecting existing measurements to the resident they affect.

## Slide 2
NeerNetra – A NAGPUR WATER TRANSPARENCY MAP
SOLUTION — CONNECT THE DATA THAT ALREADY EXISTS TO THE LOCATION WHERE PEOPLE LIVE
• Unifies 395 verified measurements from CGWB and CSIR-NEERI in one locality-scale map.
• Point click → standards-based verdict, measured values, sample period and source.
• Location search → nearest measurement + distance; unmeasured areas stay explicitly grey.
• Crop + location → CPCB irrigation class and FAO-29 crop yield-loss comparison.
• Citizen readings can add local evidence, visually distinct and never treated as drinking-water certification.
WHAT MAKES IT DIFFERENT
Resolution, provenance and uncertainty are visible on the screen — not hidden in a report.
395
real measurement points
63
CGWB sites exceed ≥1 IS 10500 limit
21/23
river sites below CPCB Class D DO line
91%
orange yield-loss at Belgaon preset; cotton 0%

## Slide 3: TECHNICAL APPROACH
TECH STACK & DATA FLOW
Published sources
CGWB CSIR-NEERI IS 10500 / CPCB / FAO-29
Normalization
Units + provenance GeoJSON / CSV
Verdict layer
Python reference engine → JS port + equivalence test
Web app
Vite + React MapLibre / Leaflet
OFFLINE-FIRST
Data bundled into the build; local tiles/libs; no live API dependency during the demo.
NO DATABASE / NO ML
Client-side computations over verified data. No predictive ML path and no invented water-safety score.
PRIVACY + TRACEABILITY
Source and sample period shown with every point; private/citizen locations are coarsened.
395 points • 35 crops • 749 supply zones • 31 reported flood locations

## Slide 4: PRACTICAL IMPLEMENTATION
IMPLEMENTATION & 3-MINUTE DEMO PATH
CHALLENGE → MITIGATION
1
Map loads sparse
395 points; everything else grey.
2
Click a measured point
Verdict first, numbers second, source always.
3
Click a grey location
“No measurement exists for this location.”
4
Belgaon preset
Orange ~91% yield loss vs cotton 0%.
5
Submit a reading
Grey area resolves into a distinct citizen point.
Fragmented sources
Standardize units, preserve provenance, use the reconciled figures.
Venue Wi-Fi / offline
Bundle data + vendor libraries + local map tiles.
Overclaim risk
Exact three-state verdicts; no interpolation; source/date always visible.
Privacy
No names on results; coarsen private/citizen locations.
Easy
Easy to use UI and access the data.

## Slide 5: IMPACT AND BENEFITS
IMPACT, BENEFITS & SDG ALIGNMENT
RESIDENTS
Find the nearest measured point, its distance, date and source — without pretending unmeasured areas are known.
NMC / ENGINEERS
Turn scattered reports and datasets into one operational view with traceable evidence.
PLANNERS / RESEARCHERS
Reveal where measurement coverage is sparse and where water-quality constraints matter for irrigation.
CITIZENS
Add local readings without exposing names or overstating what a low-cost meter can detect.
WHAT THE CURRENT EVIDENCE ALREADY SHOWS
347
CGWB groundwater samples
12 / 12
city groundwater points with coliform contamination
21 / 23
river sites below CPCB Class D DO threshold
~175 MLD
current untreated sewage (reconciled)
Proposed SDG alignment: SDG 6 • SDG 11 • SDG 16

## Slide 6: RESEARCH AND REFERENCES
• Central Ground Water Board (CGWB) — 347 district groundwater points
• CSIR-NEERI / NMC Environment Status Report 2023–24 — rivers, city groundwater and STPs
• IS 10500:2012 — drinking-water reference limits
• CPCB Designated Best Use criteria — water-use / irrigation classification
• FAO-29 crop salt-tolerance data — crop yield-loss comparison
• NMC Monsoon Preparedness Plan 2023 — 66 official low-lying flood areas
• MPCB Oct 2025 MPR — reconciled STP operational / construction figures
• OCW intervention evidence + project verification files (RECONCILIATION / AI-BUILD-CONTEXT)
EVIDENCE PRINCIPLE
No invented composite water-quality score; no spatial interpolation; every displayed claim must remain traceable to a source, standard, or observed report.
All quantitative figures above follow the project reconciliation document; older conflicting figures are intentionally excluded.